Monster iCruze
LCD Display
for the Raspberry Pi
and
Microcontrollers
It won’t replace your big display
but it has some handy uses!

---
Ta dah!
Monster® iCruze® LCD Display

---
Hardware Overview
- LCD with Hitachi HD44780 controller
  - 20x2 LCD display
  - White on Blue display
  - LED backlighting
- Attached PC board
  - AVR ATTiny26L controller
  - 5-volt regulator
- Nice looking case with ball joint
- Peel cover from bottom for sticky pad
- 4 ½-foot “telephone” cable

---
Modifications
- Reprogram the ATTiny26L controller with Mark Sproul’s firmware
  (link at the end)
- Bypass the 5-volt regulator
- Remove RJ-11 connector and replace with insulation displacement-style connector with 0.1-inch spacing

---
Wiring
- 4 wires from the display
  - Red – +5-volts (6–9-volts IFF you remove the jumper)
  - Black – Ground
  - Yellow – TTL-serial receive (by display)
  - Green – TTL-serial transmit (by display)
- Cut off green wire
- Serial data with 3–5-volts

---
Raspberry Pi Connections
For a four socket connector to use
with the RPi:
- Pin 2 – +5-volts (not used)
- Pin 4 – +5-volts
- Pin 6 – Ground
- Pin 8 – Serial port (TX)
  Raspberry Pi Serial is 3.3-volts
  which works just fine with a
  5-volt system for transmission.

---
Attaching Display
- The connector only goes on
  ONE ROW of pins – the row
  closest to the long side of
  the Raspberry Pi

---
Testing
- Powerup display should read:
  Hacked iCruze
  by KB2ICI_
  If not then check +5v and Ground connections.
- Enable RPi console but w/out a login shell.
- Now try sending some text:
  echo -e “\fTesting 1..2..3” > /dev/ttyAMA0
  Should see:
  Testing 1..2..3
  _

---
Programming
- Programs can be written in ANYTHING that suits your fancy! C, Python, shell, or even BASIC!
- Programs can open the file ‘/dev/ttyAMA0’ or ‘/dev/serial0’ or redirect the output as we did in our test
- Best to run as a non-root user (e.g. ‘pi’) but user must be in the ‘dialup’ group
- Baud rate needs to be 9600-bps
  stty -F /dev/ttyAMA0	# to check
  sudo stty -F /dev/ttyAMA0 9600	# to set

---
File: lcd_scripts
- This script must be run with /bin/bash (#!/bin/bash provided)
  - /bin/sh is usually linked to ‘dash’ on the Pi
  - I use little shell tricks that ‘dash’ can’t handle
- \016 and \017 (^N & ^O) enable/disable the upper 128 chars of the Hitachi character ROM
- Change WIFI and ETH if you use the “predictable network interface names” (or disable that B.S.)

---
Autostart on boot
- Preferred method is: Edit your crontab with
  crontab -e
- Add this line at the bottom
  @reboot	/home/pi/lcd_scripts
- This method has the advantage of running as a non-root user
- Make sure script file has ‘x’ bits set
     chmod +x lcd_scripts

---
Links
- avr-developers.com/icruze/
  - Schematics
  - Source code for Atmel microcontroller code
  - ‘avrdude’ commands for programming ATTiny chip
- www.sparkfun.com/datasheets/LCD/HD44780.pdf
  - Spec sheet for LCD display