GPIO
Presented to the Dallas Pi Sig
By
Ernest Barnes
On
February 18, 2017

---
What Does GPIO Mean?
- It is an abbreviation for General Purpose Input and Output
- The Raspberry Pi has GPIO2-27, brought out to the 40 pin GPIO header

---
How can they be used?
- GPIO outputs can be used to turn devices on and off
- GPIO inputs can be used to determine if devices are on or off
- Any/All pins can be used for either an input or output
- Some groups of pins work together

---
Some warnings about
current and voltage limits
- Voltages applied to inputs or outputs should not exceed 3.3 VDC
- Current from any one output should be limited to 16 mA

---
How to Connect LEDs and Switches
- Turn an LED on or off (LEDs are output devices)
- Check to see if a switch is open or closed (Switches are input devices)

---
Using PWM
(Pulse Width Modulation)
- Light dimmers
- Motor speed control

---
Using GPIO under (Python) program control
- It is possible to control the GPIO pins under script control, but I am not going to cover that.
- GPIO Library
- GPIOZero Library (I recommend using the gpiozero library, since it is easier to use, but included examples based on the gpio library, since you might encounter programs using it.)

---
Where do I find more information about how to use the GPIO and gpiozero libraries?
- For gpiozero, go to:
- https://gpiozero.readthedocs.io/en/v1.3.1/
- For GPIO, go to:
- https://sourceforge.net/p/raspberry-gpio-python/wiki/Examples/

---
GPIO Connector Pin Assignment
(Uses BCM numbering)

---
Wiring:
1. LED
2. Switch
3. Motor
4. 5 V TTL Output
Note: I changed my mind. Connect the switch to ground

---
Connecting an LED and Switch using a prototyping board

---
Wiring a motor (and a TTL circuit)

---
The gpiozero library provides support and examples for many different devices. These include:
- LEDs
- RGB LEDs (These have 3 LEDs bult into a single package with a common pin)
- PWMLEDs
- Switches (they call them buttons, as in push buttons). There are several different ways provided to use push button switches.
- Reversible DC motors
- Analog to Digital Converters

---
The gpiozero library provides support and examples for many different devices. These include:
- Servo motors (These rotate by angular displacement)
- Stepper motors (Don't seem to be provided. These also rotate by angular displacement)
- Ultrasonic distance measuring devices
- And there may even be more...

---
Other GPIO Pin Groups
- I2c
  - SDA(GPIO2)
  - SCL(GPIO3)
- uart
  - TXD(GPIO14)
  - RXD(GPIO15)

---
SPI (Serial Peripheral Interface):
- Can be provided either in hardware or in software. The SPI Interface must be enabled using the Raspberry Pi Configuration Utility before the hardware version can be used. I have seen warnings that the software implementation of SPI may not work with some devices.
- Pin Assignment:
  - MOSI(GPIO10): Master Out-Slave in
  - MISO(GPIO9): Master In-Slave Out
  - SCLK(GPIO11): Provides timing for data transfers
  - CE0(GPIO8): Device 0 Select
  - CE1(GPIO7): Device 1 Select

---
Other GPIO Pin Groups
- pcm
  - CLK(GPIO18)
  - DIN(GPIO20)
  - DOUT(GPIO21)
  - FS(GPIO19)